# Introduction
This document explains how to get What Is What communicate with binary-based devices (modbus, S7, etc).
# The flow

This flow has been created with node v10.16.0 and Node-RED v0.20.7.
### Third party dependencies
A Mqtt broker must be running. See mqttBroker file for more information.
In this example we do communication with binary-based Siemens S7 PLC. This is just an example, and it would work as well with any binary-based devices (for example a modbus-enabled PLC). Instead of using node-red-contrib-s7, we use here node-red-contrib-s7-comm because it’s using PLC’s raw buffers.
To test this example, we recommend to use a S7 PLC, but a simulator may be good enough. You can find one in Snap7 library, available here https://freefr.dl.sourceforge.net/project/snap7. Snap7 v1.4.1 has been successfully tested.
### Explanation
This flow demonstrates how to use binary nodes to read/write buffers from/to Siemens S7 PLC. The same kind of solution could be used with modbus or any other communication device based on binary data (with adaptation to specific data format like string, date,...).
Our goal is to handle the following PLC’s data structure.
Name	Offset	Size (byte)	Type
qtyMachine	1	4	Double integer
pauseMachine	5	1	Byte
errorMachine	6	2	Integer
speed	8	2	Integer
Reserved	10	1
id	11	52 (2 bytes header + 50 characters)	String
desc	63	92 (2 bytes header + 90 characters)	String
prodId	155	52(2 bytes header + 50 characters)	String
qty	207	4	Double integer
qtyProduced	211	4	Double integer
start	215	18 (2 bytes header + 16 characters)	String
end	233	18 (2 bytes header + 16 characters)	String

Binary node
This node builds a buffer from an object or vice-versa.
While creating the template, keep in mind that variables are following each others, that means there is no offset.
Numbers are easy to declare: “b” for big-endian, “l” for little-endian and the size in bit(s) (see javascript packet documentation for more information: http://bigeasy.github.io/packet).
On Siemens S7 PLC, data are :
- stored using big-endian,
- strings are made of a 2 bytes header (1st byte: max string’s length, 2nd byte: current string’s length) followed by the string’s characters in ASCII. This header will have to be extracted when reading and created when writing. Further more, when strings don’t fill their whole space, they may be filled with space characters (32 ASCII code).
To create a string buffer, there are 2 different possibilities:
- what we call “normal mode” : do not fill the unused characters with “space”,
- what we call the “fill space mode” : fill unused characters with “space”.
Here is the binary’s setting when s7 node is set to read from byte 1, for both modes :
Name	Normal mode	Fill space mode
qtyMachine	b32
pauseMachine	b8
errorMachine	b16
speed	b16
reserved	x8
id	b8[52]	b8[52]{32}z
desc	b8[92]	b8[92]{32}z
prodId	b8[52]	b8[52]{32}z
qty	b32
qtyProduced	b32
start	b8[18]	b8[18]{32}z
end	b8[18]	b8[18]{32}z

### First line of the flow (see above)
The first line simulates a message from What Is What. It is needed only in this example, and is not relevant in production. The inject node sends a JSON object that could have been sent by What Is What.
### Second line of the flow (see above)
The second line shows the reception of a message from a Mqtt broker. The message is sent to a Wiw2ValuesObject node which will cast it into a new message (see wiw2ValuesObject documentation). Then convert Node-RED to S7 casts it into a message compatible with binary node, which creates a buffer compatible with S7 PLC.
The inject node is used to read current data from PLC. The binary node then casts it into a JSON object compatible with valuesObject2Wiw (see valuesObject2Wiw documentation).
#### Note
Please make sure to use the right Mqtt broker settings in the Mqtt client setup.